## Slide 1: Project: Home Irrigation Control System (HICS) Team: SmartGrass
CSE Senior Design I Detailed Design Specification
January 28th , 2015
Belachew
Haile-Mariam
Gautam
Adhikari
Jeremiah
O’Connor
Tung
Vo
Notes: This presentation demonstrates the new capabilities of PowerPoint and it is best viewed in Slide Show. These slides are designed to give you great ideas for the presentations you’ll create in PowerPoint 2010!
For more sample templates, click the File tab, and then on the New tab, click Sample Templates.

## Slide 2: Architecture Overview
1
Gautam

## Slide 3: Architecture Overview

## Slide 4: Module Decomposition

## Slide 5: Producer-Consumer Matrix
 | Consumer | Soil Moisture Reading Collector | Soil Moisture Sensor Control Board | Temperature Reading Collector | Temperature Sensor Control Board | Rain Status Collector | Rain Sensor Control Board | Analog-Digital Converter | Sensor Data Packager | Serial Data Sender | Relay Module | Irrigation Valve(s) | Command Executor | Serial Data Receiver | USB/Serial Interface | JSON Message Builder | Valve Command Processor | API Caller | Response Parser | JSON Converter | URI Authenticator | Web Services | Response Handler | DB Interface | Stored Procedures | Database | Controller | Model | View | User/Admin
Producer |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Soil Moisture Reading Collector |  |  | CMRC1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Soil Moisture Sensor Control Board |  |  |  |  |  |  |  | CB1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Temperature Reading Collector |  |  |  |  | TRC1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Temperature Sensor Control Board |  |  |  |  |  |  |  | CB2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Rain Status Collector |  |  |  |  |  |  | RSC1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Rain Sensor Control Board |  |  |  |  |  |  |  | CB3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Analog-Digital Converter |  |  |  |  |  |  |  |  | ADC1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sensor Data Packager |  |  |  |  |  |  |  |  |  | SDP1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Serial Data Sender |  |  |  |  |  |  |  |  |  |  |  |  |  |  | RDS1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Relay Module |  |  |  |  |  |  |  |  |  |  |  | RM1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Irrigation Valve(s) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Command Executor |  |  |  |  |  |  |  |  |  |  | CE1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Serial Data Receiver |  |  |  |  |  |  |  |  |  |  |  |  | SDR1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
USB/Serial Interface |  |  |  |  |  |  |  |  |  | USI1 |  |  |  |  |  | USI2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
JSON Message Builder |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | JMB1 |  |  |  |  |  |  |  |  |  |  |  | 
Valve Command Processor |  |  |  |  |  |  |  |  |  |  |  |  |  |  | VCP1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
API Caller |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | AC1 |  |  |  |  |  |  |  |  |  | 
Response Parser |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | RP1 |  |  |  |  |  |  |  |  |  |  |  |  | 
JSON Converter |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | JC1 |  |  |  |  |  |  |  |  | 
URI Authenticator |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | UA2 |  | UA1 |  |  |  |  |  | 
Web Services |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | WS2 | WS1 |  |  |  |  |  | 
Response Handler |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | RH1 |  |  |  |  |  |  |  |  |  |  | 
DB Interface |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | DB4 | DB3 |  |  | DB2 |  | DB1 |  |  | 
Stored Procedures |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | SP1 |  | SP2 |  |  |  | 
Database |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | D1 |  |  |  |  | 
Controller |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | C2 |  |  |  |  | C1 | 
Model |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | M1 |  |  | 
View |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | V2 |  |  | V1
User/Admin |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | U1 | 

## Slide 6: SYSTEM HARDWARE DESCRIPTION
2
Tung

## Slide 7: System Hardware Description
Raspberry Pi
Model | Raspberry Pi B+
SoC | Broadcom BCM2835
CPU | 700 MHz ARM1176JZF -S core
GPU | 250 MHz Broadcom IV
RAM | 512
USB | 4x 2.0 Onboard USB ports
Video Out | HDMI up to 1920x1200 resolution, PAL, NTSC
Audio Out | 3.5mm Jack, HDMI
Storage | Onboard SD/MM/SDIO card slot
Networking | 10/100mbps Ethernet, RJ-45
Peripherals | GPIO, UART, SPI, IIC +3.3V, +5.0V
Power | 700 mA, 5V via MicroUSB or GPIO header
OS | Raspbian

## Slide 8: System Hardware Description
Model | Arduino Mega ATmega1289
Analog Input Pin | 16
Digital I/O Pins | 54 (of which 14 provide PWM output)
SRAM | 8K
EEPROM | 4KB
Clock Speed | 16MHz
UART Port | 3
I2C | Port
USB port | 1
Operating Voltage | 5V
Adruino Mega

## Slide 9: System Hardware Description
Model | SaintSmart 8-Channel Relay
Operating Voltage | 5V
Operating Current | 20mA
Relay Current/Voltage | AC250V 10A, DC 30V 10A
Interface | Arduino Raspberry Pi, ARM, PIC, DSP
Relay Module

## Slide 10: System Hardware Description
Model | TOOGOO Soil Moisture Sensor
Operating Voltage | 3.3V-5V
Digital Output | Yes
Analog Output | Yes
Adjustable Sensitivity | Yes
Soil Moisture Sensor

## Slide 11: System Hardware Description
Model | DS18B20 Temperature Sensor
Operating Voltage | 3.3V-5V
Analog Output | Yes
Adjustable Resolution | Yes
Temperature Sensor

## Slide 12: System Hardware Description
Model | DS18B20 Temperature Sensor
Operating Voltage | 3.3V-5V
Digital Output | Yes
Adjustable Resolution | Yes
Rain Sensor

## Slide 13: System Hardware Description
Model | CanaKit 2.5A Micro USB Power Supply
Voltage | 5V
Current | 2.5A
AC Power Module

## Slide 14: System Software Description
3
Jeremiah

## Slide 15: System Software Description
ASP.NET MVC 5
.NET Framework 4.5
Razor View Engine 3.0
Entity Framework 6
HICS Web Application

## Slide 16: System Software Description
Raspberry Pi
Rasbian OS
Processing 2.2.1
Arduino Mega
Arduino Programming Language
APL standard libraries
HICS Hardware Software

## Slide 17: SENSOR LAYER
4
Billy

## Slide 18: Rain Sensor Subsystem
Rain Status Collector
Control Board
Rain
Status Collector
Rain Sensor Subsystem
RSC1
CB3
(Analog-Digital Converter)
Source | Sink | Input to Sink | Return from Sink
Rain Status Collector | Control Board | Analog voltage | None
Interfaces

## Slide 19: Rain Sensor Subsystem
Control Board
Control Board
Rain
Status Collector
Rain Sensor Subsystem
RSC1
CB3
(Analog-Digital Converter)
Source | Sink | Input to Sink | Return from Sink
Rain Status Collector | Control Board | Analog voltage | None
Interfaces
Control Board
Rain
Status Collector
Source | Sink | Input to Sink | Return from Sink
Rain Status Collector | Control Board | Analog voltage | None
Control Board | Analog-Digital Converter | Analog voltage | None

## Slide 20: Temperature Sensor Subsystem
Temperature Reading Collector
Control Board
Temperature Reading Collector
Temperature Sensor Subsystem
TRC1
CB2
(Analog-Digital Converter)
Source | Sink | Input to Sink | Return from Sink
Temperature Reading Collector | Control Board | Analog voltage | None
Interfaces

## Slide 21: Temperature Sensor Subsystem
Control Board
Source | Sink | Input to Sink | Return from Sink
Rain Status Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
Temperature Reading Collector | Control Board | Analog voltage | None
Control Board | Analog-Digital Converter | Analog voltage | None
Control Board
Temperature Reading Collector
Temperature Sensor Subsystem
TRC1
CB2
(Analog-Digital Converter)
Temperature
Reading Collector
Control Board

## Slide 22: Soil Moisture Sensor Subsystem
Soil Moisture Reading Collector
Control Board
Soil Moisture Reading Collector
Soil Moisture Sensor Subsystem
SMRC1
CB1
(Analog-Digital Converter)
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces

## Slide 23: Soil Moisture Sensor Subsystem
Control Board
Control Board
Soil Moisture Reading Collector
Soil Moisture Sensor Subsystem
SMRC1
CB1
(Analog-Digital Converter)
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Control Board
Soil Moisture Reading Collector

## Slide 24: Hardware I/o Layer
5
Billy

## Slide 25: Sensor Controller Subsystem
Analog-Digital Converter
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Serial Data Sender
Analog-Digital Converter
Sensor Data Packager
Sensor Controller Subsystem
SDS1
SDP1
ADC1
CB1
CB2
CB3
(Control Board)
(Control Board)
(Control Board)
(USB/Serial Interface)
Source | Sink | Input to Sink | Return from Sink
Control Board(s) | Analog-Digital Converter | Analog voltage | None
Analog-Digital Converter | Sensor Data Packager | Float/double values for sensor readings | None

## Slide 26: Sensor Controller Subsystem
Sensor Data Packager
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Serial Data Sender
Analog-Digital Converter
Sensor Data Packager
Sensor Controller Subsystem
SDS1
SDP1
ADC1
CB1
CB2
CB3
(Control Board)
(Control Board)
(Control Board)
(USB/Serial Interface)
Source | Sink | Input to Sink | Return from Sink
Analog-Digital Converter | Sensor Data Packager | Float/double values for sensor readings | None
Sensor Data Packager | Serial Data Sender | String of sensor reading values | None
Sensor Data Packager
Analog-Digital Converter

## Slide 27: Sensor Controller Subsystem
Serial Data Sender
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Serial Data Sender
Analog-Digital Converter
Sensor Data Packager
Sensor Controller Subsystem
SDS1
SDP1
ADC1
CB1
CB2
CB3
(Control Board)
(Control Board)
(Control Board)
(USB/Serial Interface)
Source | Sink | Input to Sink | Return from Sink
Sensor Data Packager | Serial Data Sender | String of sensor reading values | None
Serial Data Sender | USB/Serial Interface | String of sensor reading values | None
Analog-Digital Converter
Serial Data Sender

## Slide 28: Valve Controller Subsystem
Relay Module
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
Command Executor | Relay Module | 0V(Low) or 5V(High) | None
Relay Module | Irrigation Valve(s) | 0V(off) or 24V(on) | None
Serial
Data Receiver
Relay Module
Command Executor
Valve Controller Subsystem
USI1
SDR1
CE1
RM1
(USB/Serial Interface)
(Irrigation Valves)

## Slide 29: Valve Controller Subsystem
Command Executor
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
Serial Data Receiver | Command Executor | Valve/pin number and boolean value | None
Command Executor | Relay Module | 0V(Low) or 5V(High) | None
Serial
Data Receiver
Relay Module
Command Executor
Valve Controller Subsystem
USI1
SDR1
CE1
RM1
(USB/Serial Interface)
(Irrigation Valves)
Command Executor
Relay Module

## Slide 30: Valve Controller Subsystem
Serial Data Receiver
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
USB/Serial Interface | Serial Data Receiver | Byte (to be read in as a String) | None
Serial Data Receiver | Command Executor | Valve/pin number and boolean value | None
Serial
Data Receiver
Relay Module
Command Executor
Valve Controller Subsystem
USI1
SDR1
CE1
RM1
(USB/Serial Interface)
(Irrigation Valves)
Relay Module
Serial
Data Receiver

## Slide 31: INTERFACE LAYER
6
Tung

## Slide 32: Service Caller Subsystem
Response Parser
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
Response Parser | Valve Command Processor | JSON command object | None
Response Handler | Response Parser | JSON command object or status code | None
API
Caller
Response
Parser
Service Caller Subsystem
RH1
RP1
AC1
(Valve Command Processor)
(JSON Message Builder)
JMB1
(Response Handler)
(JSON Converter)

## Slide 33: Service Caller Subsystem
API Caller
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
JSON Message Builder | API Caller | JSON object with sensor data | None
API Caller | JSON Converter | HTTP request | None
API
Caller
Response
Parser
Service Caller Subsystem
RH1
RP1
AC1
(Valve Command Processor)
(JSON Message Builder)
JMB1
(Response Handler)
(JSON Converter)
Response
Parser
API
Caller

## Slide 34: Data Processing Subsystem
USB/Serial Interface
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
USB/Serial Interface | Serial Data Receiver | Serial data byte string with irrigation control command | None
Serial Data Sender | USB/Serial Interface | Serial data string with sensor readings | None
USB/Serial Interface
JSON
Message Builder
Valve
Command Processor
Data Processing Subsystem
RP1
VCP1
JMB1
USI2
(Response Parser)
(API Caller)
SDS1
USI1
(Serial Data Receiver)
(Serial Data Sender)

## Slide 35: Data Processing Subsystem
JSON Message Builder
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
USB/Serial Interface | JSON Message Handler | Serial data string with sensor readings | None
JSON Message Handler | API Caller | JSON object | None
USB/Serial Interface
JSON
Message Builder
Valve
Command Processor
Data Processing Subsystem
RP1
VCP1
JMB1
USI2
(Response Parser)
(API Caller)
SDS1
USI1
(Serial Data Receiver)
(Serial Data Sender)
JSON
Message Builder
USB/Serial Interface

## Slide 36: Data Processing Subsystem
Valve Command Processor
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
Response Parser | Valve Command Processor | JSON command object | None
Valve Command Processor | Serial Data Receiver | Serial data string with command data | None
USB/Serial Interface
JSON
Message Builder
Valve
Command Processor
Data Processing Subsystem
RP1
VCP1
JMB1
USI2
(Response Parser)
(API Caller)
SDS1
USI1
(Serial Data Receiver)
(Serial Data Sender)
USB/Serial Interface
Valve
Command Processor

## Slide 37: SERVER LAYER
7
Jeremiah

## Slide 38: Web Application Subsystem
Model
Interfaces
Source | Sink | Input to Sink | Return from Sink
Model | Controller | A new view model or a model that represents existing data | None
Model
View
Controller
Web Application Subsystem
U1
V1
V2
C1
C2
M1
DB1
(User)
(DB Interface)
Model
View

## Slide 39: Web Application Subsystem
View/UI
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
Response Parser | Valve Command Processor | JSON command object | None
Valve Command Processor | Serial Data Receiver | Serial data string with command data | None
Model
View
Controller
Web Application Subsystem
U1
V1
V2
C1
C2
M1
DB1
(User)
(DB Interface)
Source | Sink | Input to Sink | Return from Sink
User/Admin | View/UI | Keyboard, click, or touch event | HTML view update or alert message
View/UI | User/Admin Web or Mobile Browser | HTML view with HICS system information or user information (if admin) | None
Controller | View/UI | HTML page with new or existing view model | None
View/UI | Controller | Web form or click event | HTML view or JSON message

## Slide 40: Web Application Subsystem
Controller
Source | Sink | Input to Sink | Return from Sink
Soil Moisture Reading Collector | Control Board | Analog voltage | None
Interfaces
Source | Sink | Input to Sink | Return from Sink
Response Parser | Valve Command Processor | JSON command object | None
Valve Command Processor | Serial Data Receiver | Serial data string with command data | None
Model
View
Controller
Web Application Subsystem
U1
V1
V2
C1
C2
M1
DB1
(User)
(DB Interface)
Source | Sink | Input to Sink | Return from Sink
User/Admin | View/UI | Keyboard, click, or touch event | HTML view update or alert message
View/UI | User/Admin Web or Mobile Browser | HTML view with HICS system information or user information (if admin) | None
Controller | View/UI | HTML page with new or existing view model | None
View/UI | Controller | Web form or click event | HTML view or JSON message
View
Controller
Source | Sink | Input to Sink | Return from Sink
DB Interface | Controller | User data represented by a domain object or data structure | None
Model | Controller | A view model | None
View/UI | Controller | An updated model state or request parameters | Requested data, an HTML view, or an error message
Controller | DB Interface | A new/updated model state or request parameters | Requested data in the form of a domain object or data structure
Controller | View/UI | An HTML view with corresponding view model | None

## Slide 41: Web Services Subsystem
Source | Sink | Input to Sink | Return from Sink
JSON Converter | URI Authenticator | Sensor reading object(s) and system id | None
API Caller | JSON Converter | HTTP request | None
JSON Converter
Response Handler
URI Authenticator
JSON Converter
Web
Services
Web Services Subsystem
DB3
DB4
WS1
UA1
WS2
JC1
RH1
UA2
AC1
(Response Parser)
(API Caller)
(DB Interface)
(DB Interface)
Interfaces
Response Handler
JSON Converter

## Slide 42: Web Services Subsystem
Source | Sink | Input to Sink | Return from Sink
URI Authenticator | Web Services | Sensor reading object(s) and system id | None
URI Authenticator | DB Interface | HICS system id | User domain object or null
JSON Converter | URI Authenticator | Sensor reading object(s) and system id | None
DB Interface | URI Authenticator | User domain object or null | None
URI Authenticator
Response Handler
URI Authenticator
JSON Converter
Web
Services
Web Services Subsystem
DB3
DB4
WS1
UA1
WS2
JC1
RH1
UA2
AC1
(Response Parser)
(API Caller)
(DB Interface)
(DB Interface)
Interfaces
Response Handler
URI Authenticator

## Slide 43: Web Services Subsystem
Source | Sink | Input to Sink | Return from Sink
URI Authenticator | Web Services | Environment sensor readings as objects and HICS system Id | None
DB Interface | Web Services | Command state object or thrown exception | None
Web Services | Response Handler | Command object or status string | None
Web Services | DB Interface | Environment sensor readings as objects and HICS system Id | Thrown exception or list of previous command states
Web Services
Response Handler
URI Authenticator
JSON Converter
Web
Services
Web Services Subsystem
DB3
DB4
WS1
UA1
WS2
JC1
RH1
UA2
AC1
(Response Parser)
(API Caller)
(DB Interface)
(DB Interface)
Interfaces
Response Handler
Web
Services

## Slide 44: Web Services Subsystem
Response Handler
Response Handler
URI Authenticator
JSON Converter
Web
Services
Web Services Subsystem
DB3
DB4
WS1
UA1
WS2
JC1
RH1
UA2
AC1
(Response Parser)
(API Caller)
(DB Interface)
(DB Interface)
Interfaces
Source | Sink | Input to Sink | Return from Sink
Response Parser | Valve Command Processor | JSON command object | None
Valve Command Processor | Serial Data Receiver | Serial data string with command data | None

## Slide 45: Database Interface Subsystem
Source | Sink | Input to Sink | Return from Sink
Store Procedures | DB Interface | Requested domain object(s) | None
Stored Procedures | Database | SQL query | SQL table data
Store Procedures
Interfaces
DB Interface
Database Interface Subsystem
DB1
DB2
DB3
DB4
SP1
WS1
UA1
DB1
(Controller)
C2
(Web Services)
(URI Authenticator)
(DB)
SP2
Stored Proc.
Source | Sink | Input to Sink | Return from Sink
Store Procedures | DB Interface | Requested domain object(s) | None
Stored Procedures | Database | SQL query | SQL table data
Database | Store Procedures | SQL table data | None
DB Interface | Store Procedures | Domain object(s) | Thrown exception

## Slide 46: Database Interface Subsystem
Source | Sink | Input to Sink | Return from Sink
Store Procedures | DB Interface | Requested domain object(s) | None
Stored Procedures | Database | SQL query | SQL table data
DB Interface
Interfaces
DB Interface
Database Interface Subsystem
DB1
DB2
DB3
DB4
SP1
WS1
UA1
DB1
(Controller)
C2
(Web Services)
(URI Authenticator)
(DB)
SP2
Stored Proc.
DB Interface
Stored Proc.
Source | Sink | Input to Sink | Return from Sink
DB Interface | Store Procedure | Domain object(s) or query parameters | Requested domain object(s), void, or thrown exception
DB Interface | Web Services | List of command state objects | None
DB Interface | URI Authenticator | Matching user object or null | None
DB Interface | Controller | Domain object(s) | None
Stored Procedures | DB Interface | Database table data | None
Controller | DB Interface | Domain object(s) or query parameters | Requested domain object(s), void, or thrown exception
Web Services | DB Interface | Sensor reading objects or command request | List of command state objects or thrown exception
URI Authenticator | DB Interface | HICS system id | Matching user object or null

## Slide 47: QUALITY ASSURANCE
8
Gautam

## Slide 48: Quality Assurance
  Each software components source code will be tested and to check for errors in its expected functionality
  The web application and API will utilize dependency injection to improve unit testing
Integration Testing
  In addition to individual component testing the HICS system will be tested as a whole after each component is intergrated
Unit Testing

## Slide 49: Quality Assurance
Sensor Testing: Environment sensors must be strong enough to handle radical conditions like high wind, high/low temperatures, and pressure
Web Application Testing: Must be fast and responsive and the UI must scale appropriately based on the type of device
Database Testing: The database must be able to invoke the store procedure calls and manage the serialization of transactions
Component Testing

## Slide 50: Quality Assurance
Test Cases
Test Case | Expected Result
Rain sensor detects rain | Rain status will be changed to “True”. The user sees notification on the web browser.
Soil moisture level is very low (dry) | Web browser notifies the user the amount of soil moisture and suggests watering.
User schedules watering | Watering occurs on the scheduled time and it is notified to the user on the web browser.
Temperature sensor detects change | Updated temperature will be relayed and stored in the database and the new temperature will be updated on the users web browser.

## Slide 51: REQUIREMENTS TRACABILITY
9
Jeremiah

## Slide 52: Requirements Traceability
Sensor Layer
Requirements No. | Requirements Name | Soil Moisture Sensor S/S |  | Temperature Sensor S/S |  | Rain Sensor S/S | 
 |  | Voltage Comparator | Soil Moisture Reading Collector | Voltage Comparator | Temperature Reading Collector | Voltage Comparator | Rain Status Collector
3.1 | Central Control Unit | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
3.2 | Soil Moisture Sensors | ✔ | ✔ |  |  |  | 
3.3 | Web Application |  |  |  |  |  | 
3.4 | Water Scheduler | ✔ | ✔ |  |  | ✔ | ✔
3.5 | Soil Moisture Reports | ✔ | ✔ |  |  |  | 
3.6 | User Login |  |  |  |  |  | 
3.8 | Rain Sensor |  |  |  |  | ✔ | ✔
3.10 | DB Management System | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
3.14 | Temperature Sensor |  |  | ✔ | ✔ |  | 
5.1 | Sensor Accuracy | ✔ | ✔ |  |  | ✔ | ✔
5.2 | Rain Detection |  |  |  |  | ✔ | ✔
5.3 | Comm. Between Web and Unit |  |  |  |  |  | 
8.2 | Browser Support |  |  |  |  |  | 

## Slide 53: Requirements Traceability
Hardware I/O Layer
Requirements No. | Requirements Name | Sensor Controller S/S |  |  | Valve Controller S/S |  | 
 |  | Analog-Digital Converter | Sensor Data Packager | Serial Data Sender | Relay Module | Command Executor | Serial Data Receiver
3.1 | Central Control Unit | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
3.2 | Soil Moisture Sensors | ✔ |  |  |  |  | 
3.3 | Web Application |  |  |  |  |  | 
3.4 | Water Scheduler | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
3.5 | Soil Moisture Reports | ✔ | ✔ | ✔ |  |  | 
3.6 | User Login |  |  |  |  |  | 
3.8 | Rain Sensor | ✔ | ✔ | ✔ |  |  | 
3.10 | DB Management System | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
3.14 | Temperature Sensor | ✔ | ✔ | ✔ |  |  | 
5.1 | Sensor Accuracy | ✔ | ✔ | ✔ |  |  | 
5.2 | Rain Detection | ✔ | ✔ | ✔ |  |  | 
5.3 | Comm. Between Web and Unit |  |  |  |  |  | 
8.2 | Browser Support |  |  |  |  |  | 

## Slide 54: Requirements Traceability
Requirements No. | Requirements Name | Data Processing S/S |  |  | Service Caller S/S | 
 |  | USB/Serial Interface | Valve Command Processor | JSON Message Builder | Response Parser | API Caller
3.1 | Central Control Unit | ✔ | ✔ | ✔ | ✔ | ✔
3.2 | Soil Moisture Sensors | ✔ |  | ✔ |  | ✔
3.3 | Web Application |  |  |  |  | 
3.4 | Water Scheduler | ✔ | ✔ | ✔ | ✔ | ✔
3.5 | Soil Moisture Reports | ✔ |  | ✔ |  | ✔
3.6 | User Login |  |  |  |  | 
3.8 | Rain Sensor | ✔ |  | ✔ |  | ✔
3.10 | DB Management System | ✔ | ✔ | ✔ | ✔ | ✔
3.14 | Temperature Sensor | ✔ |  | ✔ |  | ✔
5.1 | Sensor Accuracy |  |  |  |  | 
5.2 | Rain Detection | ✔ |  | ✔ |  | ✔
5.3 | Comm. Between Web and Unit |  |  |  | ✔ | ✔
8.2 | Browser Support |  |  |  |  | 
Interface I/O Layer

## Slide 55: Requirements Traceability
Requirements No. | Requirements Name | Data Processing S/S |  |  | Service Caller S/S | 
 |  | USB/Serial Interface | Valve Command Processor | JSON Message Builder | Response Parser | API Caller
3.1 | Central Control Unit | ✔ | ✔ | ✔ | ✔ | ✔
3.2 | Soil Moisture Sensors | ✔ |  | ✔ |  | ✔
3.3 | Web Application |  |  |  |  | 
3.4 | Water Scheduler | ✔ | ✔ | ✔ | ✔ | ✔
3.5 | Soil Moisture Reports | ✔ |  | ✔ |  | ✔
3.6 | User Login |  |  |  |  | 
3.8 | Rain Sensor | ✔ |  | ✔ |  | ✔
3.10 | DB Management System | ✔ | ✔ | ✔ | ✔ | ✔
3.14 | Temperature Sensor | ✔ |  | ✔ |  | ✔
5.1 | Sensor Accuracy |  |  |  |  | 
5.2 | Rain Detection | ✔ |  | ✔ |  | ✔
5.3 | Comm. Between Web and Unit |  |  |  | ✔ | ✔
8.2 | Browser Support |  |  |  |  | 
Server Layer
Requirements No. | Requirements Name | Web Services S/S |  |  |  | Database Interface S/S |  | Web Application S/S |  | 
 |  | JSON Converter | URI Authenticator | Web Services | Response Handler | DB Interface | Store Procedures | Controller | Model | UI/View
3.1 | Central Control Unit |  |  |  |  |  |  |  |  | 
3.2 | Soil Moisture Sensors |  |  |  |  |  |  |  |  | 
3.3 | Web Application | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
3.4 | Water Scheduler |  |  | ✔ | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
3.5 | Soil Moisture Reports |  |  |  |  | ✔ | ✔ | ✔ | ✔ | ✔
3.6 | User Login |  |  |  |  | ✔ | ✔ | ✔ | ✔ | ✔
3.8 | Rain Sensor |  |  |  |  |  |  |  |  | 
3.10 | DB Management System |  |  |  |  | ✔ | ✔ |  |  | 
3.14 | Temperature Sensor |  |  |  |  |  |  |  |  | 
5.1 | Sensor Accuracy |  |  |  |  |  |  |  |  | 
5.2 | Rain Detection |  |  |  |  |  |  |  |  | 
5.3 | Comm. Between Web and Unit | ✔ | ✔ | ✔ | ✔ |  |  |  |  | 
8.2 | Browser Support |  |  |  |  |  |  |  |  | ✔

## Slide 56: ACCEPTANCE PLAN
10
Gautam

## Slide 57: Acceptance Plan
HICS will be packaged with the following items:
(1) Raspberry Pi micro controller
(2) Arduino Mega 2560
(3) Soil moisture sensors
(1) Rain sensor
(1) Thermal sensor
(1) Raspberry Pi AC adapter
(1) Power adaptor for Relay Board
(1) User manual
Packaging and Installation

## Slide 58: Acceptance Plan
The Web Application must be able to create, edit, or delete user accounts and preferences
The Web Application must be able to provide a scalable UI for desktop and mobile devices
The system must be able to store sensor readings and display them on the UI
The system must be able to control the irrigation valves, and show their status on the UI
Acceptance Criteria

## Slide 59: Acceptance Plan
The Web Application must be able to allow creation of watering schedules.
The system must be able to turn on or turn off watering automatically based on conditions in the users settings.
The system must be able to turn off automatically when it loses the Internet connection, detects rainfall, or detects freezing conditions.
Acceptance Criteria

## Slide 60: Appendix
11
Gautam

## Slide 61: Appendix
Raspbian OS
Raspbian is a Debian based operating system optimized for the Raspberry Pi hardware.
It comes with over 35,000 packages which are precompiled
GSON Library
GSON library is systems library that serializes and deserializes JSON to Java objects
JQuery Library
JQuery is a JavaScript library that allows to more customization when it comes to frontend design and UI interactions
Sockets Library
The Sockets library makes the communication between Python and Java via internet using TCP/IP
Operating Systems & Libraries

## Slide 62: Appendix
Processing
Processing will be used for programming the micro-controller because it offers easy and quality programming
SQL
The SQL query language will be used to handle data queries with the HICS MYSQL database
C#
All Web Application and API programming will be developed using C#
Programming Languages

## Slide 63: Appendix
HTML/JavaScript/CSS
HTML, JavaScript, and CSS will all be used to program the styling and design of the Web Application pages
Arduino Programming Language
Arduino utilizes a native programming language, much like C, to develop programs for the microcontroller. This programming language will be used for all the Arduino microcontroller programming
Programming Languages

## Slide 64: Any Questions?
?